## Slide 1: Freshman Training Course Signal
NCTU NSS-Lab 2018
Cheng-Fa Huang
2018.08.16 @NCTU EC-543
Willy Cheng-Fa Huang

## Slide 2: Outline
Channel
Friis Transmission Equation
RFID

## Slide 3: Outline
Channel
Friis Transmission Equation
RFID
Channel

## Slide 4: Signal Representation
General form
Called the canonical representation of a
band-pass signal
amplitude
frequency
phase
s(t)
Q
I
a(t)
a(t)
Notes: 這是訊號 gerneral form
IQ domain 上表示
Band pass 訊號典型表示式
還有很多表示訊號的式子

## Slide 5: Linear Channels
Change to Cartesianor Rectangular Form
Amplitude and Phase
Notes: ＩＱ座標 轉換 笛卡爾坐標系
ampl. Phase 轉換
Time -> FFT -> freq. 𝜔=2𝜋𝑓

## Slide 6: Linear Channels
Change to Cartesianor Rectangular Form
Time domain to Frequency domain
Polar Form
Notes: 用 剛剛的轉換與 cos 相加 公式拆解
可得笛卡爾座標
Time -> FFT -> freq. 有些地方會寫
今天 focus 這部分 channel
Time -> FFT -> freq. 𝜔=2𝜋𝑓

## Slide 7: Channel
Signal is sent in time domain, but processed in frequency domain.
Signal in frequency domain
Channel
Phase
Notes: Time domain 送
Frequency domain 分析
記好 channel and phase 的長相

## Slide 8: Phase Delay
Phase delay in frequency domain is the delay in time domain.
Notes: 頻域的 phase delay 就是時域的延遲
從第二式可得
P(f) 就是 phase delay

## Slide 9: Channel Fading
Fluctuation of the local mean:
Large-scale fading
Fluctuation of the local mean:
Small-scale fading
: transmission power
: received power
Notes: 時域的訊號圖 送出與接收 power 的比值圖
較大的模型波動稱為 large scale fading
較小的模型波動稱為 small scale fading

## Slide 10
Small-Scale Fading
Notes: 先介紹 small scale fading

## Slide 11: Channel Fading
Mobility
  Slow Fading
  Fast Fading
Multipath
  Flat Fading
  Frequency-selective Fading
Notes: 主要以兩種原因分成四種 fading

## Slide 12: Channel Fading
Mobility
  Slow Fading
  Fast Fading
Multipath
  Flat Fading
  Frequency-selective Fading
Mobility
  Slow Fading
  Fast Fading
Notes: 在這先介紹以移動影響 channel 的其中兩種 fading

## Slide 13: Channel Fading
Coherence Time v.s. Doppler Spread
Coherence Time : the time duration over which the channel impulse response is considered to be not varying
Doppler Spread : the difference between the Doppler shifts of two paths
Notes: 因為是 移動的影響 所以頻域方面會考慮 Doppler 效應
Coherence time 就是一段時間 channel impulse response 沒有改變
Tc Ds 成反比

## Slide 14: Channel Fading
FFT
iFFT
Coherence time
Doppler Spread
Slow Fading
Symbol time
Signal bandwidth
Time Domain
Frequency Domain
Notes: 先定義 threshold Tc Ds
Symbol time < Tc W>Ds slow

## Slide 15: Channel Fading
FFT
iFFT
Fast Fading
Symbol time
Signal bandwidth
Time Domain
Frequency Domain
Coherence time
Doppler Spread
Notes: 相反地就是 fast

## Slide 16: Channel Fading
Mobility
  Slow Fading
  Fast Fading
Multipath
  Flat Fading
  Frequency-selective Fading
Multipath
  Flat Fading
  Frequency-selective Fading
Notes: 接下來介紹以 multipath 影響 channel 的其中兩種 fading

## Slide 17: Channel Fading
Coherence Bandwidth v.s. Delay Spread
Coherence Bandwidth : the approximate maximum bandwidth over which two frequencies of a signal are likely to experience comparable
Delay Spread : the difference between the propagation delay of two paths

## Slide 18: Channel Fading
iFFT
FFT
Coherence Bandwidth
Delay Spread
Flat Fading
Signal bandwidth
Symbol time
Frequency Domain
Time Domain

## Slide 19: Channel Fading
iFFT
FFT
Coherence Bandwidth
Delay Spread
Frequency-selective
Fading
Signal bandwidth
Symbol time
Frequency Domain
Time Domain

## Slide 20
Large-Scale Fading

## Slide 21: Path Loss
Linear path loss of the channel is the ratio of transmit
power to receive power.
The power of received signal is averaged over any random
variations due to shadowing.
Shadowing is the effect that the received signal power
fluctuates due to objects obstructing the propagation path
between tx and rx.

## Slide 22: Outline
Channel
Friis Transmission Equation
RFID
Friis Transmission Equation

## Slide 23: Why Friis’ Formula
Dispense with the usage of directivity or gain when describing antenna performance
Descriptor of antenna capture area
Notes: 通常會用 gain 表達天線的 performance
Friis 認為現有的公式都太多係數要記
Capture area 展現 free space radio circuit 的特色

## Slide 24: Friis’ Original Formula
: power available at rx antenna output terminals
: power fed into the tx antenna input terminals
: the effective area of rx antenna
: the effective area of tx antenna
d : distance between antennas
: wavelength

## Slide 25: Contemporary Formula
Few follower of Friis
Replacing the effective antenna areas with directivity counterparts yields

## Slide 26: Contemporary Formula
Notes: D_{t} and D_{r} are the antenna directivities
the antenna directivities are linear values

## Slide 27: Directivities
Notes: 看個角度的訊號最強

## Slide 28: Isotropic Radiator
Notes: 點來源

## Slide 29
Notes: 最後還是加入了 directivity 來呈現天線的效能

## Slide 30: Channel Fading Summary
Small-scale fading
  Doppler spread
    Slow fading
    Fast fading
  Delay spread
    Flat fading
    Frequency-selective fading
Large-scale fading
  Path loss
    Shadowing
Multipath
Mobility

## Slide 31
Demo

## Slide 32: Outline
Channel
Friis Transmission Equation
RFID
RFID

## Slide 33
Basic Elements

## Slide 34: RFID Standard
Bar code
  Traditional wireless
  identification
  Defacement
  Line of sight
  Manual manipulation
  Read separately
Radio Frequency IDentification
  Brand new wireless
  identification
  RF based communication
  Non-line of sight
  System based operation
  Read simultaneously

## Slide 35: RFID Reading Frequency
Frequency | Price range | Read Range | Limitations | Applications
Low Frequency 125-134 kHz | low | Low ( < 1 m.) | Low reading speed | Animal tracking
High Frequency 13.56 Mhz | Low to Middle | Low ( < 1.5 m) | Problems with metal | Library, access control
Ultra-high Freq. 860-930 MHz | Middle to High | High ( > 10 m) | Interference problems | Vehicle tracking
Microwave 2.4 GHz | High | High ( > 50 m) | Not widely deployed | Vehicle access control

## Slide 36: RFID Reading Frequency
MHz
FCC開放RFID頻段
中華電信
Up link
中華電信
Down link
RFID
915
928
922
910
895
940
955
960
902
遠傳
DL
遠傳
UP
891.4
937
892
增頻
增頻
國內RFID頻段

## Slide 37: RFID Setting
Tag Type | Reading Distance | Characteristic
Passive | < 4m | Battery free Cheap
Active | > 100m | Battery loaded Expensive

## Slide 38: RFID Setting
Tag Type | Reading Distance | Characteristic
Passive | < 4m | Battery free Cheap
Active | > 100m | Battery loaded Expensive

## Slide 39: RFID Setting

## Slide 40: RFID Setting

## Slide 41
Protocol

## Slide 42: Backscatter
Notes: A reader transmits information to a tag by modulating an RF signal

## Slide 43: Backscatter
Notes: A reader transmits information to a tag by modulating an RF signal

## Slide 44: Backscatter
Notes: The tag receives both down-link information and the entirety of its
operating energy from this RF signal.

## Slide 45: Backscatter
Power
Command
Notes: The tag receives both down-link information and the entirety of its
operating energy from this RF signal.

## Slide 46: Backscatter
Power
Carrier Wave
Notes: The reader transmits a continuous RF wave (CW) which assures that
the tag remains powered

## Slide 47: Backscatter
Notes: The tag then transmits its response by modulating the reflection coefficient of its antenna.

## Slide 48: Backscatter
Notes: The tag then transmits its response by modulating the reflection coefficient of its antenna.

## Slide 49: Backscatter
Notes: The reader is able to decode the tag response by detecting the variation in the reflected CW.

## Slide 50: Backscatter
Notes: The reader is able to decode the tag response by detecting the variation in the reflected CW.

## Slide 51: Backscatter
Notes: The reader is able to decode the tag response by detecting the variation in the reflected CW.

## Slide 52: UHF EPC
Physical Layer
  RFID tags communicate by “backscattering” signals that are concurrent with reader transmissions, and use a variety of frequencies and encodings under the control of the reader.
MAC Layer
  Readers and tags use a variation on slotted Aloha to solve the multi-access problem in a setting where readers can hear tags but tags cannot hear each other.

## Slide 53: FM0

## Slide 54: FM0
Preamble
1
0
1
0
v
1
Notes: Find some examples

## Slide 55: MAC Layer
Based on Framed Slotted Aloha
  Each frame has a number of slots
  Each tag will reply in one randomly selected slot per frame
  The number of slots in the frame is determined by the reader and can be varied on a per frame basis

## Slide 56: Query round

## Slide 57
Notes: 找實際訊號圖

## Slide 58: RN16
Preamble
RN16
1
0
0
0
1
0
0
0
1
0
0
1
0
0
0
0
Notes: Find some examples

## Slide 59: Query round
Query Round
  an individual frame : Query Cycle
  the series of Query Rounds between power down periods
The reader can optionally transmit a Select command
Limits the number of active tags by providing a bit mask only tags with ID’s (or memory locations) that match this mask will respond in the subsequent round

## Slide 60: Query round
Query Round
  an individual frame : Query Cycle
  the series of Query Rounds between power down periods
The reader can optionally transmit a Select command
Limits the number of active tags by providing a bit mask only tags with ID’s (or memory locations) that match this mask will respond in the subsequent round

## Slide 61: Query round
A Query command is transmitted which contains the fields:
  Determine the up-link frequency and data encoding : the Q parameter and a Target parameter.
  A tag receives a Query command, it chooses a random number in the range (0, ), where 0 ≤ Q ≤ 15, and the value is stored in the slot counter of the tag. The tag changes its Inventoried flag.

## Slide 62: Query round
A Query command is transmitted which contains the fields:
  Determine the up-link frequency and data encoding : the Q parameter and a Target parameter.
  A tag receives a Query command, it chooses a random number in the range (0, ), where 0 ≤ Q ≤ 15, and the value is stored in the slot counter of the tag. The tag changes its Inventoried flag.

## Slide 63: Query round
If a tag stores a 0 in its slot counter, it will transmit a 16 bit random number (RN16) immediately.
The reader will echo the RN16 in an ACK packet after receiving it.
If the tag successful receives the ACK with the correct random number, the tag will backscatter its ID.

## Slide 64: Query round
If a tag stores a 0 in its slot counter, it will transmit a 16 bit random number (RN16) immediately.
The reader will echo the RN16 in an ACK packet after receiving it.
If the tag successful receives the ACK with the correct random number, the tag will backscatter its ID.

## Slide 65: Query round
The reader will send a QueryRepeat command to cause the tag to toggle its Inventoried flag.
  If the ID was not successfully received by the reader, a NAK command is sent which resets the tag so that a subsequent QueryRepeat will not result in Inventoried flag being changed.
  A QueryRepeat signals the end of the slot.

## Slide 66: Query round
The reader will send a QueryRepeat command to cause the tag to toggle its Inventoried flag.
  If the ID was not successfully received by the reader, a NAK command is sent which resets the tag so that a subsequent QueryRepeat will not result in Inventoried flag being changed.
  A QueryRepeat signals the end of the slot.

## Slide 67: Query round
On receiving the command, the remaining tags will:
  Decrement their slot counter
  Respond with a RN16 if their slot counter is set to 0.
  The process then repeats, with the number of QueryRepeats being equal to the number of slots set using the Q parameter.

## Slide 68: Query round
Notes: 撞掉失敗，或是沒有人倒數到 0

## Slide 69: Related Work
Fundamental
  Michael Buettner , David Wetherall An empirical study of UHF RFID performance. 14th ACM Int. Conf. on MobiCom
  EPCglobal. Epc radio-frequency identity protocols class-1 generation-2 uhf rfid protocol for communications at 860 mhz-960 mhz version 2.0.0. , 2013

## Slide 70: Related Work
Localization
  Jue Wang, Dina Katabi Dude, where's my card?: RFID positioning that works with multipath and non-line of sight. the ACM SIGCOMM, 2013
Tracking
  Lei Yang, Yekui Chen Tagoram: Real-Time Tracking of Mobile RFID Tags to High Precision Using COTS Devices. ACM Int. Conf. on MobiCom, 2014
Device-free
  Chuyu Wang, Jian Liu, Yingying Chen Multi-Touch in the Air: Device-Free Finger Tracking and Gesture Recognition via COTS RFID. IEEE Infocom, 2018

## Slide 71: Related Work
Search tags
  Jihong Yu, Wei Gong, Jiangchuan Liu Fast and Reliable Tag Search in Large-Scale RFID Systems: A Probabilistic Tree-based Approach. IEEE Infocom, 2017
Find missing/unknown tags
  Muhammad Shahzad, Alex X. Liu Fast and Reliable Detection and Identification of Missing RFID Tags in the Wild. IEEE/ACM Transactions on Networking, 2016
Find moving tag
  Chuyu Wang, Lei Xie, Wei Wang Moving Tag Detection via Physical Layer Analysis for Large-Scale RFID Systems. IEEE INFOCOM, 2016

## Slide 72: Reference
https://www.flaticon.com/
https://www.sitebuilderreport.com/stock-up
https://en.wikipedia.org/wiki/Friis_transmission_equation
https://en.wikipedia.org/wiki/Path_loss
https://ccrma.stanford.edu/~jos/fp/Phase_Delay.html
https://en.wikipedia.org/wiki/Communication_channel
https://en.wikipedia.org/wiki/Fading
http://www.sengpielaudio.com/calculator-timedelayphase.html
EPC RFID protocols Class-1 Gen2 UHF RFID protocol for communications
An empirical study of UHF RFID performance