## Slide 1: Freshman Training Course Signal
NCTU NSS-Lab 2018
Cheng-Fa Huang
2018.08.16 @NCTU EC-543
Willy Cheng-Fa Huang

## Slide 2: Outline
Channel
Friis Transmission Equation
RFID

## Slide 3: Outline
Channel
Friis Transmission Equation
RFID
Channel

## Slide 4: Signal Representation
General form
Called the canonical representation of a
band-pass signal
amplitude
frequency
phase
s(t)
Q
I
a(t)
a(t)
Notes: 這是訊號 gerneral form
IQ domain 上表示
Band pass 訊號典型表示式
還有很多表示訊號的式子

## Slide 5: Linear Channels
Change to Cartesianor Rectangular Form
Amplitude and Phase
Notes: ＩＱ座標 轉換 笛卡爾坐標系
ampl. Phase 轉換
Time -> FFT -> freq. 𝜔=2𝜋𝑓

## Slide 6: Linear Channels
Change to Cartesianor Rectangular Form
Time domain to Frequency domain
Polar Form
Notes: 用 剛剛的轉換與 cos 相加 公式拆解
可得笛卡爾座標
Time -> FFT -> freq. 有些地方會寫
今天 focus 這部分 channel
Time -> FFT -> freq. 𝜔=2𝜋𝑓

## Slide 7: Channel
Signal is sent in time domain, but processed in frequency domain.
Signal in frequency domain
Channel
Phase
Notes: Time domain 送
Frequency domain 分析
記好 channel and phase 的長相

## Slide 8: Phase Delay
Phase delay in frequency domain is the delay in time domain.
Notes: 頻域的 phase delay 就是時域的延遲
從第二式可得
P(f) 就是 phase delay

## Slide 9: Channel Fading
Fluctuation of the local mean:
Large-scale fading
Fluctuation of the local mean:
Small-scale fading
: transmission power
: received power
Notes: 時域的訊號圖 送出與接收 power 的比值圖
較大的模型波動稱為 large scale fading
較小的模型波動稱為 small scale fading

## Slide 10
Small-Scale Fading
Notes: 先介紹 small scale fading

## Slide 11: Channel Fading
Mobility
  Slow Fading
  Fast Fading
Multipath
  Flat Fading
  Frequency-selective Fading
Notes: 主要以兩種原因分成四種 fading

## Slide 12: Channel Fading
Mobility
  Slow Fading
  Fast Fading
Multipath
  Flat Fading
  Frequency-selective Fading
Mobility
  Slow Fading
  Fast Fading
Notes: 在這先介紹以移動影響 channel 的其中兩種 fading

## Slide 13: Channel Fading
Coherence Time v.s. Doppler Spread
Coherence Time : the time duration over which the channel impulse response is considered to be not varying
Doppler Spread : the difference between the Doppler shifts of two paths
Notes: 因為是 移動的影響 所以頻域方面會考慮 Doppler 效應
Coherence time 就是一段時間 channel impulse response 沒有改變
Tc Ds 成反比

## Slide 14: Channel Fading
FFT
iFFT
Coherence time
Doppler Spread
Slow Fading
Symbol time
Signal bandwidth
Time Domain
Frequency Domain
Notes: 先定義 threshold Tc Ds
Symbol time < Tc W>Ds slow

## Slide 15: Channel Fading
FFT
iFFT
Fast Fading
Symbol time
Signal bandwidth
Time Domain
Frequency Domain
Coherence time
Doppler Spread
Notes: 相反地就是 fast

## Slide 16: Channel Fading
Mobility
  Slow Fading
  Fast Fading
Multipath
  Flat Fading
  Frequency-selective Fading
Multipath
  Flat Fading
  Frequency-selective Fading
Notes: 接下來介紹以 multipath 影響 channel 的其中兩種 fading

## Slide 17: Channel Fading
Coherence Bandwidth v.s. Delay Spread
Coherence Bandwidth : the approximate maximum bandwidth over which two frequencies of a signal are likely to experience comparable
Delay Spread : the difference between the propagation delay of two paths
Notes: 針對 multipath 由兩個指標做判斷
Coherence Bandwidth : 兩訊號大致最大的頻寬
Delay Spread : 兩段路徑的 propagation delay 的差距

## Slide 18: Channel Fading
iFFT
FFT
Coherence Bandwidth
Delay Spread
Flat Fading
Signal bandwidth
Symbol time
Frequency Domain
Time Domain
Notes: 訊號在頻域的比閥值小而時域超過 delay spread

## Slide 19: Channel Fading
iFFT
FFT
Coherence Bandwidth
Delay Spread
Frequency-selective
Fading
Signal bandwidth
Symbol time
Frequency Domain
Time Domain
Notes: 相反稱為 Frequency-selective Fading

## Slide 20
Large-Scale Fading
Notes: 前面介紹的是 small scale fading
接下來介紹 large scale fading

## Slide 21: Path Loss
Linear path loss of the channel is the ratio of transmit
power to receive power.
The power of received signal is averaged over any random
variations due to shadowing.
Shadowing is the effect that the received signal power
fluctuates due to objects obstructing the propagation path
between tx and rx.
Notes: 看 Path loss 主要是看送出比上收到的能量
收到的訊號會受到 fading 的影響稱為 shadowing
最常見的就是 tx rx 間的傳送路徑有東西阻擋

## Slide 22: Outline
Channel
Friis Transmission Equation
RFID
Friis Transmission Equation
Notes: 針對 path loss 的描述
Friis 提出一個公式來表達

## Slide 23: Why Friis’ Formula
Dispense with the usage of directivity or gain when describing antenna performance
Descriptor of antenna capture area
Notes: 通常會用 gain 表達天線的 performance
Friis 認為現有的公式都太多係數要記
Capture area 展現 free space radio circuit 的特色

## Slide 24: Friis’ Original Formula
: power available at rx antenna output terminals
: power fed into the tx antenna input terminals
: the effective area of rx antenna
: the effective area of tx antenna
d : distance between antennas
: wavelength
Notes: 單純用可以量測的數據描述收到及送出訊號的能量比值

## Slide 25: Contemporary Formula
Few follower of Friis
Replacing the effective antenna areas with directivity counterparts yields
Notes: 但後來大家都不用 有效天線面積 而改用 antenna directivities
D 的介紹投影片有，有興趣可自行閱讀

## Slide 26: Contemporary Formula
Notes: D_{t} and D_{r} are the antenna directivities
the antenna directivities are linear values

## Slide 27: Directivities
Notes: 看個角度的訊號最強 以 D 表示之

## Slide 28: Isotropic Radiator
Notes: dBi 的 ｉ的意思是 從點來源發散出的訊號的 能量（dB）

## Slide 29
Notes: 從一開始有效天線面積到最後常用的 directivity 來呈現天線的效能

## Slide 30: Channel Fading Summary
Small-scale fading
  Doppler spread
    Slow fading
    Fast fading
  Delay spread
    Flat fading
    Frequency-selective fading
Large-scale fading
  Path loss
    Shadowing
Mobility
Multipath
Notes: Small scale
以 time domain 來分類，Doppler mobility Delay multipath
Large scale
Path loss shadowing

## Slide 31
Demo
Notes: 看 matlab 小示範

## Slide 32
Notes: 剛剛畫出來的圖是 圓形的原因

## Slide 33: Outline
Channel
Friis Transmission Equation
RFID
RFID
Notes: 最後一部份是介紹我目前的研究

## Slide 34
Basic Elements
Notes: 基礎設備介紹

## Slide 35: RFID Standard
Bar code
  Traditional wireless
  identification
  Defacement
  Line of sight
  Manual manipulation
  Read separately
Radio Frequency IDentification
  Brand new wireless
  identification
  RF based communication
  Non-line of sight
  System based operation
  Read simultaneously
Notes: 最傳統最常見的無線辨識碼是所謂的 bar code
雖然很方便，但卻有許多缺點必須很近、表面必須乾淨、LOS
LOS tx 與 rx 之間沒有障礙物
RFID tag 可以同時很多一起讀 NLOS 不易毀損

## Slide 36: RFID Reading Frequency
Frequency | Price range | Read Range | Limitations | Applications
Low Frequency 125-134 kHz | low | Low ( < 1 m.) | Low reading speed | Animal tracking
High Frequency 13.56 Mhz | Low to Middle | Low ( < 1.5 m) | Problems with metal | Library, access control
Ultra-high Freq. 860-930 MHz | Middle to High | High ( > 10 m) | Interference problems | Vehicle tracking
Microwave 2.4 GHz | High | High ( > 50 m) | Not widely deployed | Vehicle access control
Notes: Tag 有幾種不同的讀取頻率
目前主要是用 Ultra high freq.

## Slide 37: RFID Reading Frequency
MHz
FCC開放RFID頻段
中華電信
Up link
中華電信
Down link
RFID
915
928
922
910
895
940
955
960
902
遠傳
DL
遠傳
UP
891.4
937
892
增頻
增頻
國內RFID頻段
Notes: 每個頻段都會經過分配，目前國內使用 RFID 的頻段是 922~928 MHz
再來介紹 RFID 使用物件及特性

## Slide 38: RFID Setting
Tag Type | Reading Distance | Characteristic
Passive | < 4m | Battery free Cheap
Active | > 100m | Battery loaded Expensive
Notes: Tag 分成兩種都是靠反射來傳送訊息
Passive 利用 reader 訊號做充電
Active 就是 裝電池或有其他充電來源

## Slide 39: RFID Setting
Tag Type | Reading Distance | Characteristic
Passive | < 4m | Battery free Cheap
Active | > 100m | Battery loaded Expensive
Notes: 常用的是 passive

## Slide 40: RFID Setting
Notes: 天線基本上有兩種型態
當 reader 同時扮演 rx tx 的角色

## Slide 41: RFID Setting
Notes: 將 tag 放在不同位置會有不同的 效果
發現右邊這種放法收到的訊號比較好

## Slide 42
Protocol

## Slide 43: Backscatter
Notes: 一個 passive tag 一個 reader

## Slide 44: Backscatter
Power
Carrier Wave
Notes: Reader 會透過穩定的 carrier wave 送能量給 tag
讓 tag 有能量回傳資訊

## Slide 45: Backscatter
Notes: Reader 會根據使用者要做的指示將訊號轉成可傳送的波

## Slide 46: Backscatter
Notes: Reader 送到每個 tag

## Slide 47: Backscatter
Power
Command
Notes: Tag 同時收到能量及訊息

## Slide 48: Backscatter
Notes: 將回應轉成可送的波

## Slide 49: Backscatter
Notes: 回送給 reader

## Slide 50: Backscatter
Notes: Reader 收到來自 tag 包含回傳carrier wave 及 回復 的波

## Slide 51: Backscatter
Notes: 透過 decode 技術把 carrier wave 拿掉得到正確的 訊號

## Slide 52: Backscatter
Notes: 最後轉回可被電腦分析的訊號即完成一趟下達指令的流程

## Slide 53: UHF EPC
Physical Layer
  RFID tags communicate by “backscattering” signals that are concurrent with reader transmissions, and use a variety of frequencies and encodings under the control of the reader.
MAC Layer
  Readers and tags use a variation on slotted Aloha to solve the multi-access problem in a setting where readers can hear tags but tags cannot hear each other.

## Slide 54: FM0

## Slide 55: FM0
Preamble
1
0
1
0
v
1
Notes: Find some examples

## Slide 56: MAC Layer
Based on Framed Slotted Aloha
  Each frame has a number of slots
  Each tag will reply in one randomly selected slot per frame
  The number of slots in the frame is determined by the reader and can be varied on a per frame basis

## Slide 57: Query round

## Slide 58
Notes: 找實際訊號圖

## Slide 59: RN16
Preamble
RN16
1
0
0
0
1
0
0
0
1
0
0
1
0
0
0
0
Notes: Find some examples

## Slide 60: Query round
Query Round
  an individual frame : Query Cycle
  the series of Query Rounds between power down periods
The reader can optionally transmit a Select command
Limits the number of active tags by providing a bit mask only tags with ID’s (or memory locations) that match this mask will respond in the subsequent round

## Slide 61: Query round
Query Round
  an individual frame : Query Cycle
  the series of Query Rounds between power down periods
The reader can optionally transmit a Select command
Limits the number of active tags by providing a bit mask only tags with ID’s (or memory locations) that match this mask will respond in the subsequent round

## Slide 62: Query round
A Query command is transmitted which contains the fields:
  Determine the up-link frequency and data encoding : the Q parameter and a Target parameter.
  A tag receives a Query command, it chooses a random number in the range (0, ), where 0 ≤ Q ≤ 15, and the value is stored in the slot counter of the tag. The tag changes its Inventoried flag.

## Slide 63: Query round
A Query command is transmitted which contains the fields:
  Determine the up-link frequency and data encoding : the Q parameter and a Target parameter.
  A tag receives a Query command, it chooses a random number in the range (0, ), where 0 ≤ Q ≤ 15, and the value is stored in the slot counter of the tag. The tag changes its Inventoried flag.

## Slide 64: Query round
If a tag stores a 0 in its slot counter, it will transmit a 16 bit random number (RN16) immediately.
The reader will echo the RN16 in an ACK packet after receiving it.
If the tag successful receives the ACK with the correct random number, the tag will backscatter its ID.

## Slide 65: Query round
If a tag stores a 0 in its slot counter, it will transmit a 16 bit random number (RN16) immediately.
The reader will echo the RN16 in an ACK packet after receiving it.
If the tag successful receives the ACK with the correct random number, the tag will backscatter its ID.

## Slide 66: Query round
The reader will send a QueryRepeat command to cause the tag to toggle its Inventoried flag.
  If the ID was not successfully received by the reader, a NAK command is sent which resets the tag so that a subsequent QueryRepeat will not result in Inventoried flag being changed.
  A QueryRepeat signals the end of the slot.

## Slide 67: Query round
The reader will send a QueryRepeat command to cause the tag to toggle its Inventoried flag.
  If the ID was not successfully received by the reader, a NAK command is sent which resets the tag so that a subsequent QueryRepeat will not result in Inventoried flag being changed.
  A QueryRepeat signals the end of the slot.

## Slide 68: Query round
On receiving the command, the remaining tags will:
  Decrement their slot counter
  Respond with a RN16 if their slot counter is set to 0.
  The process then repeats, with the number of QueryRepeats being equal to the number of slots set using the Q parameter.

## Slide 69: Query round
Notes: 撞掉失敗，或是沒有人倒數到 0

## Slide 70: Related Work
Fundamental
  Michael Buettner , David Wetherall An empirical study of UHF RFID performance. 14th ACM Int. Conf. on MobiCom
  EPCglobal. Epc radio-frequency identity protocols class-1 generation-2 uhf rfid protocol for communications at 860 mhz-960 mhz version 2.0.0. , 2013

## Slide 71: Related Work
Localization
  Jue Wang, Dina Katabi Dude, where's my card?: RFID positioning that works with multipath and non-line of sight. the ACM SIGCOMM, 2013
Tracking
  Lei Yang, Yekui Chen Tagoram: Real-Time Tracking of Mobile RFID Tags to High Precision Using COTS Devices. ACM Int. Conf. on MobiCom, 2014
Device-free
  Chuyu Wang, Jian Liu, Yingying Chen Multi-Touch in the Air: Device-Free Finger Tracking and Gesture Recognition via COTS RFID. IEEE Infocom, 2018

## Slide 72: Related Work
Search tags
  Jihong Yu, Wei Gong, Jiangchuan Liu Fast and Reliable Tag Search in Large-Scale RFID Systems: A Probabilistic Tree-based Approach. IEEE Infocom, 2017
Find missing/unknown tags
  Muhammad Shahzad, Alex X. Liu Fast and Reliable Detection and Identification of Missing RFID Tags in the Wild. IEEE/ACM Transactions on Networking, 2016
Find moving tag
  Chuyu Wang, Lei Xie, Wei Wang Moving Tag Detection via Physical Layer Analysis for Large-Scale RFID Systems. IEEE INFOCOM, 2016

## Slide 73: Reference
https://www.flaticon.com/
https://www.sitebuilderreport.com/stock-up
https://en.wikipedia.org/wiki/Friis_transmission_equation
https://en.wikipedia.org/wiki/Path_loss
https://ccrma.stanford.edu/~jos/fp/Phase_Delay.html
https://en.wikipedia.org/wiki/Communication_channel
https://en.wikipedia.org/wiki/Fading
http://www.sengpielaudio.com/calculator-timedelayphase.html
EPC RFID protocols Class-1 Gen2 UHF RFID protocol for communications
An empirical study of UHF RFID performance