## Slide 1: Freshman Training Course Signal
NCTU NSS 2018
Chengfa Huang
2018.08. @NCTU EC-345
Willy Cheng-Fa Huang

## Slide 2: Outline
Channel
Friis Transmission Equation
RFID

## Slide 3: Outline
Channel
Friis Transmission Equation
RFID
Channel

## Slide 4: Signal Representation
General form
Called the canonical representation of a
band-pass signal
amplitude
frequency
phase
s(t)
Q
I
a(t)
a(t)

## Slide 5: Linear Channels
Change to Cartesianorrectangularform
Amplitude and Phase
Notes: Time -> FFT -> freq.
Time -> FFT -> freq. 𝜔=2𝜋𝑓

## Slide 6: Linear Channels
Change to Cartesianorrectangularform
Time domain to Frequency domain
polarform
Notes: Time -> FFT -> freq.
Time -> FFT -> freq. 𝜔=2𝜋𝑓

## Slide 7: Channel
Signal is sent in time domain, but processed in frequency domain.
Signal in frequency domain
Channel
Phase
Notes: Time domain 送
Frequency domain 分析

## Slide 8: Phase Delay
Phase delay in frequency domain is the delay in time domain.

## Slide 9: Channel Fading
Fluctuation of the local mean:
Large-scale fading
Fluctuation of the local mean:
Small-scale fading
: transmission power
: received power

## Slide 10
Small-Scale Fading

## Slide 11: Channel Fading
Coherence Time v.s. Doppler Spread
Coherence Time : the time duration over which the channel impulse response is considered to be not varying
Doppler Spread : the difference between the Doppler shifts of two paths

## Slide 12: Channel Fading
FFT
iFFT
Coherence time
Doppler Spread
Slow Fading
Symbol time
Signal bandwidth
Time Domain
Frequency Domain

## Slide 13: Channel Fading
FFT
iFFT
Fast Fading
Symbol time
Signal bandwidth
Time Domain
Frequency Domain
Coherence time
Doppler Spread

## Slide 14: Channel Fading
Coherence Bandwidth v.s. Delay Spread
Coherence Bandwidth : the approximate maximum bandwidth over which two frequencies of a signal are likely to experience comparable
Delay Spread : the difference between the propagation delay of two paths

## Slide 15: Channel Fading
iFFT
FFT
Coherence Bandwidth
Delay Spread
Flat Fading
Signal bandwidth
Symbol time
Frequency Domain
Time Domain

## Slide 16: Channel Fading
iFFT
FFT
Coherence Bandwidth
Delay Spread
Frequency-selective
Fading
Signal bandwidth
Symbol time
Frequency Domain
Time Domain

## Slide 17
Large-Scale Fading

## Slide 18: Path Loss
Linear path loss of the channel is the ratio of transmit
power to receive power.
The power of received signal is averaged over any random
variations due to shadowing.
Shadowing is the effect that the received signal power
fluctuates due to objects obstructing the propagation path
between tx and rx.

## Slide 19: Outline
Channel
Friis Transmission Equation
RFID
Friis Transmission Equation

## Slide 20: Why Friis’ Formula
Dispense with the usage of directivity or gain when describing antenna performance
Descriptor of antenna capture area
Notes: 通常會用 gain 表達天線的 performance
Friis 認為現有的公式都太多係數要記
Capture area 展現 free space radio circuit 的特色

## Slide 21: Friis’ Original Formula
: power available at rx antenna output terminals
: power fed into the tx antenna input terminals
: the effective area of rx antenna
: the effective area of tx antenna
d : distance between antennas
: wavelength

## Slide 22: Contemporary Formula
Few follower of Friis
Replacing the effective antenna areas with directivity counterparts yields

## Slide 23: Contemporary Formula
Notes: D_{t} and D_{r} are the antenna directivities
the antenna directivities are linear values

## Slide 24: Directivities
Notes: 看個角度的訊號最強

## Slide 25: Isotropic Radiator
Notes: 點來源

## Slide 26
Notes: 最後還是加入了 directivity 來呈現天線的效能

## Slide 27: Channel Fading Summary
Small-scale fading
  Doppler spread
    Slow fading
    Fast fading
  Delay spread
    Flat fading
    Frequency-selective fading
Large-scale fading
  Path loss
    Shadowing
Multipath
Mobility

## Slide 28
Demo

## Slide 29: Outline
Channel
Friis Transmission Equation
RFID
RFID

## Slide 30
Basic Elements

## Slide 31: RFID Standard
Bar code
  Traditional wireless
  identification
  Defacement
  Line of sight
  Manual manipulation
  Read separately
Radio Frequency IDentification
  Brand new wireless
  identification
  RF based communication
  Non-line of sight
  System based operation
  Read simultaneously

## Slide 32: RFID Reading Frequency
Frequency | Price range | Read Range | Limitations | Applications
Low Frequency 125-134 kHz | low | Low ( < 1 m.) | Low reading speed | Animal tracking
High Frequency 13.56 Mhz | Low to Middle | Low ( < 1.5 m) | Problems with metal | Library, access control
Ultra-high Freq. 860-930 MHz | Middle to High | High ( > 10 m) | Interference problems | Vehicle tracking
Microwave 2.4 GHz | High | High ( > 50 m) | Not widely deployed | Vehicle access control

## Slide 33: RFID Reading Frequency
MHz
FCC開放RFID頻段
中華電信
Up link
中華電信
Down link
RFID
915
928
922
910
895
940
955
960
902
遠傳
DL
遠傳
UP
891.4
937
892
增頻
增頻
國內RFID頻段

## Slide 34: RFID Setting
Tag Type | Reading Distance | Characteristic
Passive | < 4m | Battery free Cheap
Active | > 100m | Battery loaded Expensive

## Slide 35: RFID Setting
Tag Type | Reading Distance | Characteristic
Passive | < 4m | Battery free Cheap
Active | > 100m | Battery loaded Expensive

## Slide 36: RFID Setting

## Slide 37: RFID Setting

## Slide 38
Protocol

## Slide 39: Backscatter
Notes: A reader transmits information to a tag by modulating an RF signal

## Slide 40: Backscatter
Notes: A reader transmits information to a tag by modulating an RF signal

## Slide 41: Backscatter
Notes: The tag receives both down-link information and the entirety of its
operating energy from this RF signal.

## Slide 42: Backscatter
Power
Command
Notes: The tag receives both down-link information and the entirety of its
operating energy from this RF signal.

## Slide 43: Backscatter
Power
Carrier Wave
Notes: The reader transmits a continuous RF wave (CW) which assures that
the tag remains powered

## Slide 44: Backscatter
Notes: The tag then transmits its response by modulating the reflection coefficient of its antenna.

## Slide 45: Backscatter
Notes: The tag then transmits its response by modulating the reflection coefficient of its antenna.

## Slide 46: Backscatter
Notes: The reader is able to decode the tag response by detecting the variation in the reflected CW.

## Slide 47: Backscatter
Notes: The reader is able to decode the tag response by detecting the variation in the reflected CW.

## Slide 48: Backscatter
Notes: The reader is able to decode the tag response by detecting the variation in the reflected CW.

## Slide 49: UHF EPC
Physical Layer
  RFID tags communicate by “backscattering” signals that are concurrent with reader transmissions, and use a variety of frequencies and encodings under the control of the reader.
MAC Layer
  Readers and tags use a variation on slotted Aloha to solve the multi-access problem in a setting where readers can hear tags but tags cannot hear each other.

## Slide 50: FM0

## Slide 51: FM0
Preamble
1
0
1
0
v
1
Notes: Find some examples

## Slide 52: MAC Layer
Based on Framed Slotted Aloha
  Each frame has a number of slots
  Each tag will reply in one randomly selected slot per frame
  The number of slots in the frame is determined by the reader and can be varied on a per frame basis

## Slide 53: Query round

## Slide 54
Notes: 找實際訊號圖

## Slide 55: RN16
Preamble
RN16
1
0
0
0
1
0
0
0
1
0
0
1
0
0
0
0
Notes: Find some examples

## Slide 56: Query round
Query Round
  an individual frame : Query Cycle
  the series of Query Rounds between power down periods
The reader can optionally transmit a Select command
Limits the number of active tags by providing a bit mask only tags with ID’s (or memory locations) that match this mask will respond in the subsequent round

## Slide 57: Query round
Query Round
  an individual frame : Query Cycle
  the series of Query Rounds between power down periods
The reader can optionally transmit a Select command
Limits the number of active tags by providing a bit mask only tags with ID’s (or memory locations) that match this mask will respond in the subsequent round

## Slide 58: Query round
A Query command is transmitted which contains the fields:
  Determine the up-link frequency and data encoding : the Q parameter and a Target parameter.
  A tag receives a Query command, it chooses a random number in the range (0, ), where 0 ≤ Q ≤ 15, and the value is stored in the slot counter of the tag. The tag changes its Inventoried flag.

## Slide 59: Query round
A Query command is transmitted which contains the fields:
  Determine the up-link frequency and data encoding : the Q parameter and a Target parameter.
  A tag receives a Query command, it chooses a random number in the range (0, ), where 0 ≤ Q ≤ 15, and the value is stored in the slot counter of the tag. The tag changes its Inventoried flag.

## Slide 60: Query round
If a tag stores a 0 in its slot counter, it will transmit a 16 bit random number (RN16) immediately.
The reader will echo the RN16 in an ACK packet after receiving it.
If the tag successful receives the ACK with the correct random number, the tag will backscatter its ID.

## Slide 61: Query round
If a tag stores a 0 in its slot counter, it will transmit a 16 bit random number (RN16) immediately.
The reader will echo the RN16 in an ACK packet after receiving it.
If the tag successful receives the ACK with the correct random number, the tag will backscatter its ID.

## Slide 62: Query round
The reader will send a QueryRepeat command to cause the tag to toggle its Inventoried flag.
  If the ID was not successfully received by the reader, a NAK command is sent which resets the tag so that a subsequent QueryRepeat will not result in Inventoried flag being changed.
  A QueryRepeat signals the end of the slot.

## Slide 63: Query round
The reader will send a QueryRepeat command to cause the tag to toggle its Inventoried flag.
  If the ID was not successfully received by the reader, a NAK command is sent which resets the tag so that a subsequent QueryRepeat will not result in Inventoried flag being changed.
  A QueryRepeat signals the end of the slot.

## Slide 64: Query round
On receiving the command, the remaining tags will:
  Decrement their slot counter
  Respond with a RN16 if their slot counter is set to 0.
  The process then repeats, with the number of QueryRepeats being equal to the number of slots set using the Q parameter.

## Slide 65: Query round
Notes: 撞掉失敗，或是沒有人倒數到 0

## Slide 66: Related Work
Fundamental
  Michael Buettner , David Wetherall An empirical study of UHF RFID performance. 14th ACM Int. Conf. on MobiCom
  EPCglobal. Epc radio-frequency identity protocols class-1 generation-2 uhf rfid protocol for communications at 860 mhz-960 mhz version 2.0.0. , 2013

## Slide 67: Related Work
Localization
  Jue Wang, Dina Katabi Dude, where's my card?: RFID positioning that works with multipath and non-line of sight. the ACM SIGCOMM, 2013
Tracking
  Lei Yang, Yekui Chen Tagoram: Real-Time Tracking of Mobile RFID Tags to High Precision Using COTS Devices. ACM Int. Conf. on MobiCom, 2014
Device-free
  Chuyu Wang, Jian Liu, Yingying Chen Multi-Touch in the Air: Device-Free Finger Tracking and Gesture Recognition via COTS RFID. IEEE Infocom, 2018

## Slide 68: Related Work
Search tags
  Jihong Yu, Wei Gong, Jiangchuan Liu Fast and Reliable Tag Search in Large-Scale RFID Systems: A Probabilistic Tree-based Approach. IEEE Infocom, 2017
Find missing/unknown tags
  Muhammad Shahzad, Alex X. Liu Fast and Reliable Detection and Identification of Missing RFID Tags in the Wild. IEEE/ACM Transactions on Networking, 2016
Find moving tag
  Chuyu Wang, Lei Xie, Wei Wang Moving Tag Detection via Physical Layer Analysis for Large-Scale RFID Systems. IEEE INFOCOM, 2016

## Slide 69: Reference
https://www.flaticon.com/
https://www.sitebuilderreport.com/stock-up
https://en.wikipedia.org/wiki/Friis_transmission_equation
https://en.wikipedia.org/wiki/Path_loss
https://ccrma.stanford.edu/~jos/fp/Phase_Delay.html
https://en.wikipedia.org/wiki/Communication_channel
https://en.wikipedia.org/wiki/Fading
http://www.sengpielaudio.com/calculator-timedelayphase.html
EPC RFID protocols Class-1 Gen2 UHF RFID protocol for communications
An empirical study of UHF RFID performance